## Slide 1: Enhanced DSCP by in-band signaling for latency guaranteed service
Lin Han (lin.han@futurewei.com)
Yingzhen Qu (yingzhen.qu@futurewei.com)

## Slide 2: Introduction
In-band signaling was introduced in TSVWG
The presentation will use it to work with DSCP idea to achieve the bounded latency service
  Focus on
    the architecture, math and experiments on bounded latency service
  Not about
    In-band signaling details, TCP/UDP changes, congestion control etc.
Objective
  Provide more scalable control and data plane solution for guaranteed service, latency and bandwidth
  Provide E2E Bandwidth Guaranteed Service (BGS) and Latency Guaranteed Service (LGS)
Solution
  In-band signaling carries the user’s service expectation (Bandwidth and/or Latency)
  Network device on the path check if the resource is enough and update signaling accordingly.
  Flows will be classified according to application expectations and network resource reservation status.
    New DSCP values are needed to represent new classes, the number is TBD
  Class Based queuing and scheduling applied to the class of traffic
    For LGS flow, either the 1st or 2nd PQ are mapped.
    For BGS flow, the WRR shared Q are mapped.

## Slide 3: Design targets
Service Guarantee
  Provide guaranteed and minimized (queuing) latency for LGS (Latency Guaranteed Service) flows
    The maximum latency is guaranteed, minimized and predictable at each hop, if LGS flow rate is confirmed with their pre-claimed parameters (CIR,PIR,CBS,EBS)
  Provide guaranteed bandwidth for BGS (Bandwidth Guaranteed Service) flows
    The bandwidth of CIR is guaranteed at each hop, if BGS flow rate is confirmed with their pre-claimed parameters (CIR,PIR,CBS,EBS)
No starvation
  LGS flows will never starve other types of lower priority flows (BGS and BES)
  BGS flows will never starve BE flows
No sacrifice of link utilization
  When the total rate of LGS flow is less than the committed rate (sum of CIR of all LGS flows), other class flows (BGS and BES) can use the remained bandwidth
  When the total rate of LGS flow is less than the committed rate (sum of CIR of all LGS flows), and, the total rate of BGS flow is less than the committed rate (sum of CIR of all BGS flows), other class flows (BES) can use the remained bandwidth
Fairness within the same class
  All LGS flows will share the bandwidth within its class
  All BGS flows will share the bandwidth within its class
  All BE flows will share the bandwidth within BE class
Backward compatible with current DiffServ, and can coexist and can be deployed incrementally.

## Slide 4: Review of in-band signaling
IPv6 hdr
Payload
HbH ext hdr
HbH-aware-router
QoS dir
IPv6 hdr
Payload
Dst ext hdr
BNG
DSL
FTTH
PON
OLT
RSG
P Router
Metro Aggregation
IP Core
Backhaul
Router
Access
Mobile
AGG
L3 network
EPC
Content Provider network
CSG
PGW
PE
report
Configure to process hop-by-hop IPv6 ext hdr
Only needed for throttle devices
Signal processing distributed to NPU on line card
Per flow state kept in line card
Per flow state self-maintained by data flow, deleted if aged
Basic security for signaling and data forwarding are provided
Provider’s network, one AS

## Slide 5: Network modeling
Switch
Fabric
Ingress Traffic Classification Module at
All Ingress Routers’ ingress interface
Egress Queuing and Scheduling Module at
All Routers’ egress interface
New DSCP value is used to identify the new class for LGS flows
Rate is checked for LGS flows, colored packets are remarked to lower class or discarded
Rate is checked for LGS flows, colored packets are remarked to lower class or discarded
LGS flows are queued into the 2nd priority queue
PQ+WRR for scheduling

## Slide 6: Signaling and rules for a new connection
Switch
Fabric
Ingress Traffic Classification Module at
All Ingress Routers’ ingress interface
Egress Queuing and Scheduling Module at
All Routers’ egress interface
If (total ingress flow’s CIR < ingress interface rate)
  Allowed, classify as LGS flow, update meter DB, flow DB and in-band signaling
else
  not allowed, classified as BE, update in-band signaling
If (total egress flow’s CIR < egress interface rate)
  allowed, update meter DB, flow DB and in-band signaling
else
  not allowed, update in-band signaling
In-band signaling will notify the host about the resource reservation status on path, host then knows the status of connection

## Slide 7: Configuration: Ingress shaper at PE ingress interface

## Slide 8: Configuration: Egress shaper, queuing and scheduler at all routers egress interfaces

## Slide 9: Queuing latency estimation per hop - 1
Estimate the worst scenario conservatively per hop, thus the E2E latency can be guaranteed to be below the maximum value statistically
Only queuing delay is estimated, other delays (switching and propagation etc.) are relatively small and fixed.
Assume all packet sizes are the longest packet size
If LGS flows queued in the highest priority queue
  The maximum queue depth is
  The maximum delay of queuing at each hop is
,
is the link rate;
is the maximum packet size
is the cir for the ith LGS flow, r is the ratio of peak cir to avg cir

## Slide 10: Queuing latency estimation per hop - 2
If LGS flows queued into the 2nd highest priority queue, assume the 1st queue is EF:
  The maximum queue depth is
  The maximum delay of queuing at the hop is
,
is the link rate;
is the maximum packet size
is the cir for the ith LGS flow, r is the ratio of peak cir to avg cir
is the peak rate for EF flows from management knowledges

## Slide 11: Experiment results and analysis
Severely congested at all routers by uncontrolled BE traffic
Continuous and bursty UDP traffic is used
Most severe bottle neck for LGS
BE traffic
EF and LGS traffic

## Slide 12: Case 1: EF+LGS < 50% link rate
Theorical value(r=1)
Mean
Mean
Theorical value(r=1)
Mean
Theorical value(r=1)
Mean
Theorical value(r=1)
EF flows =4, LGS flows = 16; REF=8.14M, RLGS=26.67M; Burst traffic, Burst duration = Exp(0.02s), Burst sleep = Exp(0.001s).
Fully congested at all routers by BE, All Link Util =~100

## Slide 13: Case 2: EF+LGS 65% link rate
Mean
Theorical value(r=1)
Mean
Theorical value(r=1)
Theorical value(r=1)
Mean
Mean
Theorical value(r=1)
EF flows =4, LGS flows = 16; REF=14.385M, RLGS=50.11M; Burst traffic, Burst duration = Exp(0.02s), Burst sleep = Exp(0.001s).
Fully congested at all routers by BE, All Link Util =~100

## Slide 14: Case 3: EF+LGS link rate
Theorical value(r=1)
Mean
Mean
Theorical value(r=1)
Mean
Theorical value(r=1)
Mean
Theorical value(r=1)
EF flows =4, LGS flows = 16; REF=21.84M, RLGS=69.66M; Burst traffic, Burst duration = Exp(0.02s), Burst sleep = Exp(0.001s). Fully congested at all routers by BE, All Link Util =~100

## Slide 15: Experiment results analysis
Design targets can be satisfied by the Class Based Queuing + In-band Signaling
The queuing latency of PQ is very short, it is not impacted by the congestion of WRR queues. The latency is related to link rate: 100M ~hundreds us; 100G~ hundreds ns.
The queuing latency can be estimated with acceptable accuracy when EF+LGS flow rate is not close to the egress link rate.
The estimation accuracy may decrease when the EF+LGS flow rate is close to the egress link rate. This can be explained by the impact of the jitter of the ingress traffic rate deviated from the average rate. When the jitter of ingress rate cause the rate exceeding the link rate, packet cannot be sent out in time and will build up.

## Slide 16: Conclusion
In-band signaling
  Configuration automation for DiffServ
  Support the guaranteed service for E2E flows in a managed domain
  New service can coexist with the current DiffServ
  The current DiffServ capable hardware can be reused with minimum changes
Design targets can be satisfied
Only flow state is kept, No per flow scheduling. It is not heavy considering the new service is only a small portion of the whole network.
Further research
  To make better use of the new services, TCP CC should be improved so the BGS and LGS could have different CC.
  New meter to smooth the burst of traffic to achieve better latency and jitter
  Other technologies such as DeltaQ to smooth the bursts in network
  In-band signaling work with other queuing algorithms to achieve the LGS
  Interworking with other protocols such as TSN and Detnet

## Slide 17
Q & A